## Slide 1: GARDS A Go-Around Detection System implemented at Schiphol Airport Mariska Roerdink Project manager GARDS & Senior Performance Expert Air Traffic Control the Netherlands / Luchtverkeersleiding Nederland
Air Traffic Control
the Netherlands

## Slide 2: In case of a go-around…
What happens between
air traffic controller
and flight crew?

## Slide 3: Procedure vs. practice
ATCo instructs go-around
Flight crew initiates go-around, does not (immediately) inform ATC, ATC detects go-around
Flight crew initiates go-around, does not (immediately) inform ATC, ATC does not detect go-around
Flight crew initiates go-around and informs ATC

## Slide 4: Schiphol Airport runway layout
Dependent runway use

## Slide 5: A possible incident

## Slide 6: Continuous safety improvement
Procedure
Machine
Human
Increase detection probability
Restrict use of dependent runways
Training
Safety awareness
Timing procedures
GARDS: Go-ARound Detection System

## Slide 7: GARDS: automatic go-around detection
Surveillance
Runway
Landing
Aircraft?
Altitude / position
High speed
YES
ALERT
visual detection
YES
Non-nominal landing parameters?
pilot report

## Slide 8: GARDS operational concept
Conditions
Traffic
Alerting
System use
All runways & combinations
All visibility conditions
IFR approaches only
Visual
Auditory
Safety net
No GARDS inputs required
Cannot be switched off by ATCo
No change in working method

## Slide 9: Human Machine Interface
Visual alert
Presented on ground situation and air surveillance display.
Auditory alert
Generated at working position of the involved runway controller

## Slide 10: Technical approach

## Slide 11: System tuning: find the balance
False alerts
Timing of alerting

## Slide 12: Performance validation
Analysis based on:
More than five years of radar data
More than 1 million arrivals
More than 2000 go-arounds
False alerts
0,01 %
Timing of alerting
7 (late GA) –
15 seconds (early GA)
Go live!

## Slide 13: Implementation
Live at Schiphol control towers since May 2015
Operational evaluation in 2015
Minor update in November 2015

## Slide 14: Facts & figures
After go-live:
More than 215.000 arrivals
All go-arounds detected
10 false alerts
  Some solved by november 2015 update

## Slide 15: False alerts explained
Temporary loss of multilateration coverage
Glidepath deviation
High speed after landing
Circling approaches –
no false alert!

## Slide 16: Lessons learned – Development
Continuous involvement of controller community
Safety net part of complete package of measures
Safety net complementary to existing practice
Intuitive system
  Consistent use over runways and conditions
  Easy to explain system design

## Slide 17: Lessons learned – In practice
Positive acceptance of GARDS
Off-line tuning ensures successful go-live
Evaluation in practice for minor updates
Ground safety net introduces air-ground awareness

## Slide 18: More information?
Mariska Roerdink
Project manager GARDS
Air Traffic Control the Netherlands / Luchtverkeersleiding Nederland
 m.roerdink@lvnl.nl
 +31 20 406 2947
This project was sponsored by the Knowledge & Development Centre Mainport Schiphol