## Slide 1
Runway Collision Risk Measurement using ADS-B
Brussels
6 June 2017
Marco Merens
Chief, Integrated Aviation Analysis
Air Navigation Bureau
ICAO

## Slide 2: Runway Safety
Excursions
Collisions
Single Aircraft
Dual Aircraft
Loss of Separation
… with edge of runway
… with other aircraft/vehicle
ACFT Land/Take Off
Runway crossings
Weather
ACFT Attitude
RWY Condition
ADRM Layout
Barriers

## Slide 3: Gaining Insight
Level 1
  Reactive analysis and investigation of high consequence events (accidents, serious incidents)
Level 2
  Monitoring of everyday operations and hazards and combined realtime analysis
  Define, separate and track Normal vs Abnormal operations

## Slide 4: Level 2 Data Analysis Process
Oversight Audits
NOTAMS
METARS
Hazards
ADSB Ground Tracks
Analysis
Latitude, Longitude
Heading
Ground speed
Flight Id
ACFT Type
…by the second
Indicators
Metrics

## Slide 5: Visualizing the data
Acceleration
Deceleration
Const. Speed
Stop (0 speed)
Circle size proportional to speed
Circle center is aircraft position
Circles spaced by 1 second
HongKong VHHH

## Slide 6: Speed Marks
43kts
Exit Speed
Marks
HongKong VHHH

## Slide 7: Runway Remaining
Monitor the separation with runway end

## Slide 8: Runway Remaining
0.4g
Distances after which it is not possible to stop before the end of the runway at the given speed and deceleration
100kts
80kts
60kts
Number of landings vs speed and remaining distance for 1 day in VHHH
HongKong VHHH

## Slide 9: Runway Remaining
0.4g
100kts
80kts
60kts
Number of landings vs speed and remaining distance for 1 day in KATL
Atlanta KATL
One aircraft was at 60kts with 1000 feet remaining

## Slide 10: Reduced separation with runway end
Atlanta KATL
2000feet
1300 feet
20kts
Exit Speed

## Slide 11: Runway Crossings
2
1
0
0
1
Hong Kong
Hong Kong
Atlanta
Atlanta
Atlanta

## Slide 12: Monitoring Usage
X Crossings per Day
One day at Hong Kong RWY 07R/25L
Nb. of Crossings
Nb. of Landings
Nb. of Take-Off
Operations
per nb of Operations per 15 min
Ops Mix
Runway Availability
F

## Slide 13: Monitoring Separation
X Crossings per Day
One day at Hong Kong RWY 07R/25L
per nb of Operations per 15 min
Seconds between Crossings and Landings / Takeoffs
Seconds between Take-offs and Landings

## Slide 14: Future Work
Define Indicators relevant for monitoring of runway collision risk
Connect to ADSB data on ground level and hazard data
Automate the real-time generation of those indicators
Feed applications and visualizations via ICAO SIMS
Contact iaa@icao.int for more information and collaboration