## Slide 1: Preventing runway collisions
Sudden High Energy Runway Conflicts
(SHERC)

## Slide 2: WHat IS a sherc event ?
Sudden High Energy Runway Conflict (SHERC)
is a sub-set of Runway Incursion.
So, why make a separate study of this small area ?

## Slide 3: Why study sherc events ?
With the active cooperation of the ANSPs, EUROCONTROL studied 57 of the 110 Severity A&B Runway Incursions reported across Europe in 2014.
13 of the 57 events were classified as Severity A
3 of the 13 Severity A events were SHERC events
2 of the 3 events were resolved by last minute pilot collision avoidance
In the other event collision was avoided by providence (luck).

## Slide 4: Why study sherc events ?
Sudden High Energy Runway Collision is
Our Worst Case Scenario !
Our Nightmare !
Runway Collision was narrowly avoided 3 times in one year. That’s Why !

## Slide 5: We Need to know
What barriers currently exist to help both ATC, pilots and ground operators to avoid SHERC events?
Are these current defences as strong as reasonably practical ?
If not, Is there a quick fix?
What can be done now and in the medium term?

## Slide 6: CAN we define a sherc event ?
Not Precisely
A SHERC event typically involves a runway conflict in which, once initiated, the time available to ATC to prevent a collision is likely to be less than the time so needed.

## Slide 7: SHERC
Guidelines
Runway Occupancy occurred immediately before the Runway Incursion
Sudden to those involved
High Energy
Available Time close to or less than Needed Time
Collision Avoidance
Separation criteria at CPA
* MITRE

## Slide 8
Runway OCCUPANCY occurred immediately
before Runway INCURSION
The vehicle or second aircraft should not have been on the runway for more than 30 seconds before the “incursion” i.e. the clearance to land or take-off.
This removes events where a vehicle or aircraft has been present on the runway for some time.
* MITRE

## Slide 9: SUDDEN
In order for the event to be categorised as sudden:
A landing aircraft should be not more than 600ft/2nm final at the time of the incursion.
These accords with the FAROS acquisition protocol of 500ft.
An aircraft cleared for take-off must be already lined up at the time of the runway incursion.
* MITRE

## Slide 10: HIGH ENERGY
In the case of an aircraft taking off; it must have reached at least 80 kts at the time of pilot becoming aware of the conflict.
In the case of a landing aircraft; it must have an IAS of at least 100 kts at the time of pilot becoming aware of the conflict.
* MITRE

## Slide 11
NEEDED TIME - LANDING
ATC or Pilot may become immediately aware though visual detection.
If not, research shows that the average time for ATC to react to an alert is 6.9 secs (within one standard deviation), The same research concluded that the average time for a pilot to subsequently react is 2.3 seconds.
The average time from a systems alert to the commencement of deceleration is 9 - 10 seconds.
During this time a landing aircraft (at 130kts) will travel around 600m. (4000m / min)
Deceleration to stop with maximum braking – add another 17 seconds and 600m
NEEDED TIME from A-SMGCS alert (or similar) to landing aircraft stopping is around 26 seconds or 1200m distance.
* MITRE

## Slide 12
NEEDED TIME – ON TAKE-OFF
.
From Alert to commencement of deceleration an aircraft on take-off roll will travel approx. 280m.
Deceleration to stop with maximum braking – add another 570m
NEEDED TIME from A-SMGCS alert (or similar) is the about 21 seconds or 850m distance.
In other words, if A-SMGCS triggers less than 21 secs before CPA – the aircraft will not stop in time.
* MITRE

## Slide 13: COLLISION AVOIDANCE
There must be evidence of deliberate action taking to avoid the collision or increase the minimum distance at CPA.
A sighting report with no apparent deviation from the norm is not a SHERC.
* MITRE

## Slide 14
SEPARATION remaining at CPA
The minimum separation remaining at CPA:
not more than 500m or 400ft vertically.
* MITRE

## Slide 15: SO, HOW DOES A SHERC EVENT START 4 Scenario sources
  An incorrect ATC clearance to either an aircraft landing/taking-off, or an aircraft/vehicle on the ground resulting in an incorrect presence on the runway.
  A non-conformance with an ATC clearance by an aircraft landing/taking-off, or by an aircraft/vehicle on the ground, due to spatial/positional confusion, resulting in an incorrect presence on the runway.

## Slide 16: SO, HOW DOES A DOES SHERC EVENT START Scenario sources
  A non-conformance with ATC clearance by an aircraft landing/taking-off, or by an aircraft/vehicle on the ground, due to misinterpretation or mishear of the clearance, resulting in an incorrect presence on the runway
  A non-conformance with ATC clearance by an aircraft landing/taking-off, or by an aircraft/vehicle on the ground, due poor CRM and/or incorrect execution of the plan, resulting in an incorrect presence on the runway.

## Slide 17: Generic SITUATIONS
Landing on runway suddenly occupied
Taking-off on runway suddenly occupied
High energy conflict on intersecting runways

## Slide 18: 28 Resultant scenarios Example – Landing on a runway suddenly occupied
A1a | Runway entry by aircraft/vehicle in accordance with clearance. Shortly after, ATC incorrectly clear aircraft on short final to land.
A1b | Aircraft cleared to land on short final or landing. Aircraft/vehicle suddenly enters the runway due to it receiving an incorrect ATC clearance.
B1a | Runway entry by aircraft/vehicle in accordance with clearance. Shortly after, aircraft is on short final or landing contrary to its ATC clearance due spatial/positional confusion.
B1b | Aircraft cleared to land, on short final or landing, as an aircraft/vehicle suddenly enters the runway contrary to its ATC clearance due spatial/positional confusion.
C1a | Runway entry by aircraft/vehicle in accordance with clearance. Shortly after, aircraft lands contrary to its ATC clearance due to misinterpretation or mishear of the clearance.
C1b | Aircraft cleared to land, on short final or landing, as an aircraft/vehicle suddenly enters the runway contrary to its ATC clearance due to misinterpretation or mishearing the clearance.
D1a | Runway entry by aircraft/vehicle in accordance with clearance. Shortly after, aircraft lands contrary to its ATC clearance due poor CRM and/or incorrect execution of the plan.
D1b | Aircraft cleared to land, on short final or landing, as an aircraft/vehicle suddenly enters the runway contrary to its ATC clearance due poor CRM and/or incorrect execution of the plan.

## Slide 19: Identify potential barriers
Prevention of Sudden High Energy Runway Conflicts
These barriers, when deployed and employed correctly, are capable of alerting ATC, Pilots and Drivers in time to prevent a Runway Incursion that would be a precursor to a SHERC event
Mitigation of the outcome of Sudden High Energy Runway Conflicts
These barriers, when deployed and employed correctly, are capable of alerting ATC, Pilots and Drivers to the initial stages of a SHERC in sufficient time to act in order to prevent a collision

## Slide 20: SHERC Prevention barriers
PB1 | ATCO memory aids for runway occupancy by standardised flight data displays including dedicated runway bays, blocking strips etc.
PB2 | ATCO direct visual detection
PB3 | ATCO visual detection using remote camera displays
PB4 | Aerodrome traffic awareness including surveillance and runway incursion detection and alerting (such as A-SMGCS level 2)
PB5 | Aerodrome traffic awareness including surveillance and predictive runway incursion detection and alerting. (such as A-SMGCS levels 3 and 4)
PB6 | ATC Clearance Conformance Monitoring Alerts and Confliction Detection. Input of ATC clearances that enable the use of “early warning” surveillance and data to highlight to ATC non-conformance to clearance and the potential consequences of an incorrect clearance. PB6a: Conformance Monitoring Alerts (CMA) PB6b: Conflicting ATC Clearance Alert (CATC)

## Slide 21
PB7 | Pilot/Driver detection and report
PB8 | Final Approach Runway Occupancy Signal (FAROS.) A visual signal to aircraft on final approach to land that the runway ahead is occupied by another aircraft or a vehicle. This is done by adapting the VASI or PAPI system to alter from steady lights to flashing mode whilst the identified hazard remains
PB9 | Autonomous Runway Incursion Warning System (ARIWS) Any system which provides autonomous detection of a potential incursion or of the occupancy of an active runway and a direct warning to a flight crew or a vehicle operator. (ICAO Annexe 14) Runway status lights (RWSL) A type of ARIWS.. The two basic components of RWSL are Runway Entrance Lights (RELs) and Take-off Hold Lights (THLs). Either may be installed by itself, but the two components are designed to be complementary to each other. PB9a: Take Off Hold Lights (THLs). Positioned in the runway departure area to provide an indication to pilots and vehicle drivers that the runway is unsafe for take-off. PB9b: Runway Entrance Lights (RELs). Installed at taxiway/runway intersections commencing just before runway holding points to provide an indication when it is unsafe to enter the runway.

## Slide 22
PB10 | SmartRunway and SmartLanding: A software enhancement of RAAS available on later-model Enhanced Ground Proximity Warning Systems. In this context it provides information to pilots on which runway is ahead both airborne and on the ground.
PB11 | Airport Moving Maps PB11a: 2D with traffic. Positioned on pilot’s Navigational Display to show airfield layout, position of base aircraft and other aircraft/vehicles including direction of travel. PB11b: 3D GPS without traffic. Positioned on pilot’s Primary Flight Display. It is similar to automobile GPS but includes track, speed, and height and runway designator. PB11c: Taxi Wizard. Shows the pilot planned taxy route from apron to runway holding point. Input via Datalink or manually.
PB12 | 24H use of illuminated stop bars and robust procedures to never cross a lit stop bar and for ATC never to clear an aircraft/vehicle to cross a lit stop bar.

## Slide 23: 3D Airport moving MaP (courtesy Honeywell Inc)

## Slide 24: 2D Airport moving MaP (courtesy Honeywell Inc)

## Slide 25: SHERC Mitigation barriers
MB1 | ATCO late direct visual detection
MB2 | ATCO late visual detection using remote camera displays
MB3 | Aerodrome Surface Movement system including Runway Incursion Monitor (RIM)
MB4 | ATC Clearance Conformance Monitoring Alerts and Confliction Detection. As per Prevention barrier. MB4a: Conformance Monitoring Alerts (CMA) MB4b: Conflicting ATC Clearance Alert (CATC)
MB5 | Pilot/driver late visual detection

## Slide 26
MB6 | Sensor Controlled Incursion Projection System (SCIPS) A system alerting both ATC and the pilot/driver that a lit stop bar has been crossed.
MB7 | Autonomous Runway Incursion Warning System (ARIWS) A system which provides autonomous detection of a potential incursion or of the occupancy of an active runway and a direct warning to a flight crew or a vehicle operator. (ICAO Annexe 14) Runway status lights (RWSL) as per Prevention Barrier MB7a: Take Off Hold Lights (THLs). As per Prevention Barrier MB7b: Runway Entrance Lights (RELs). As per Prevention Barrier
MB8 | Airport Moving Maps MB8a: 2D with traffic. As per Prevention Barrier MB8b: 3D GPS without traffic. As per Prevention Barrier

## Slide 27: Barrier Matrix
 | A1a | A1b | B1a | B1b | C1a | C1b | D1a | D1b
PB1: ATCO memory aids |  |  |  |  |  |  | 3 | 
PB2: ATCO direct visual detection | 2,3 |  | 2 | 2 |  |  | 2 | 
PB3: ATCO detection using remote cameras | 2,3 |  |  | 2,3 |  |  | 2,3 | 
PB4: Aerodrome Surface Movement system including RIM level 2. | 3 |  |  |  |  |  | 3 | 
PB5: Aerodrome Surface Movement system including RIM level 3/4. |  |  | 3 |  |  |  |  | 
PB6a: Conformance Monitoring Alerts (CMA) |  |  |  | 1 |  | 1 |  | 
PB6b: Conflicting ATC Clearance Alert (CATC) |  |  |  |  |  |  |  | 
PB7: Pilot/Driver visual detection | 2,4 | 2,4 | 2,4 | 2,4 | 2,4 | 2,4 | 2,4 | 2,4
PB8: FAROS |  | 4 |  | 4 |  | 4 |  | 4
PB9a: Take Off Hold Lights (THLs). PB9b: REL |  |  |  |  |  |  |  | 
PB10: SmartRunway and SmartLanding |  |  |  | 6 |  |  |  | 4
PB11a: Airport Moving maps 2D with traffic on ND |  |  |  | 6 |  |  |  | 
PB11b: Airport Moving Maps 3D on PFD |  |  |  | 6 |  |  |  | 
PB11c: Pilot Taxi Wizard |  |  |  | 5,6 |  |  |  | 
PB12: 24H stop bars and procedure never to cross lit stop bar |  |  |  |  |  |  |  | 

## Slide 28
Barrier | Barrier Description | Score | Effectiveness
PB6 | ATC Clearance Conformance Monitoring Alerts and Confliction Detection 6a: CMA 14 6b: CATC 15 | 29 | 35 %
PB1 | ATCO memory aids | 22 | 26 %
PB9 | Autonomous Runway Incursion Warning System 9a: THL 18 9b: REL 8 Combined score: 22 | 22 | 26 %
PB11 | Airport Moving Maps 11a: 23 11b: 13 Combined score: 22 11c: 5 | 22 | 26%
PB12 | 24H Stop bars and procedure not to cross illuminated stop bar | 20 | 24 %
PB7 | Pilot/Driver Visual Detection | 16 | 19 %
PB8 | Final Approach Runway Occupancy Signal (FAROS) | 16 | 19 %
PB5 | Aerodrome Surface Movement system including Runway Incursion Monitor (RIM) functionality level 3/4. | 14 | 17 %
PB2 | ATCO direct visual detection | 13 | 15 %
PB3 | ATCO detection with remote cameras | 12 | 14 %
PB10 | SmartRunway and SmartLanding | 11 | 13 %

## Slide 29
PB6 ATC Clearance Conformance Monitoring and Confliction Detection |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB1 ATC memory aids |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB12 24H Stop bars |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB11 Airport Moving Maps |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB9 ARIWS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB8 FAROS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB5 RIM level 3/4. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB10 SmartRunway and SmartLanding |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB7 Pilot/Driver Visual Detection |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB2 ATC direct visual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB3 ATC remote cameras |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB4 Runway Incursion Monitor (RIM) level 2. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 30: Mitigation barriers
Barrier | Barrier Description | Score | Effectiveness
MB5 | Pilot/driver detection | 24 | 29 %
MB6 | Sensor Controlled Incursion Projection System | 19 | 23%
MB7 | Autonomous Runway Incursion Warning System (ARIWS) MB7a: Runway Status Lights 7 Take Off Hold Lights (THLs). 3 Combined:7 | 7 | 8 %
MB1 | ATCO late direct visual detection | 4 | 5 %

## Slide 31: Review of actual events
What were the principal Contributing factors?
What was the ACTUAL recovery barrier?
What ATC barriers were breached?
What barriers, if deployed, could have prevented the event or reduced the risk of collision?
Do the barriers acting in the real world accord with the barriers expected in the Generic Study?

## Slide 32: Example of an actual event
A CRJ700 made a high speed rejected take off upon seeing a light aircraft on the runway ahead at night. By veering to the left around it whilst decelerating, a collision was avoided.
The Cessna 172 had just landed on the same runway and, after landing had been instructed to clear right at the first exit, located at 500m from the landing threshold. Half a minute later, the controller cleared the CRJ700 for take-off and shortly after, the C172 advised that it was still on the runway having missed the turn off and asked to exit next right.
The CRJ700 crew reported that at a speed of about 110kts, they had heard the light aircraft say he had missed his turn off and the First Officer had then seen a white aircraft tail light to the right of the centreline ahead and immediately called “Abort, Abort”. They steered to the left with maximum braking and they had subsequently passed to the left of the Cessna with an estimated 3m clearance at a speed of approximately 40Kts.

## Slide 33
The controller on the TWR frequency had been certified in the TWR position a month prior to the incident. The Investigation noted that of his 80 hours training time for that certification, less than one hour was recorded as being at night. He did receive a daytime airfield tour during his training in order to orient himself with the airport layout, but he had never been out on the airport movement area at night.
He stated that he had scanned the runway before issuing the take-off clearance to the CRJ. He did not recall actually seeing the Cessna clear the runway but assumed that it vacated as he could not see it. The controller stated that he just "lost the Cessna in the lights."

## Slide 34
ATC Contributing factors:
Perception – Misperceive visual information
Decision – Incorrect plan to give take-off clearance without positive evidence of rwy clearance
Training – Lack of completeness
Training – Task familiarity
Actual Recovery Barrier:
MB5 Pilot visual detection

## Slide 35
Barriers breached:
PB2 ATC direct visual detection
PBP Correct use of ATC procedures re- runway vacation
MB1 ATC late direct visual detection
Remaining barriers available that could have reduced risk of collision:
X Nil
Barriers that, if deployed, could have prevented the runway incursion and/or reduced risk of collision:
PB9a Take Off Hold Lights

## Slide 36: Contributing factors in 19 actual events
ATC Perception x 24
Pilot Perception x 18
ATC Action x 14
ATC Memory x 11
Pilot CRM Issues x 6
Not see conflict out of the window
Not see other aircraft
Convey incomplete information
Forgot to scan
Distraction

## Slide 37: conclusions
The study concurs with and supports the FAA National Runway Safety Plan conclusion that an incorporation of multiple layers of technology is currently the most effective response to Sudden High Energy Runway Conflicts
No barrier by itself has the potential to prevent more than 35% of identified potential scenarios.
It was concluded that a combination/s of the following barriers have the highest potential to prevent Sudden High Energy Runway Conflicts.
  ATC Conformance Monitoring and Conflicting Clearances Alerts
  The correct use of ATC memory aids
  The use of stop bars 24H together with procedures never to cross an illuminated bar.
  Autonomous Runway Incursion Warning Systems (such as Runway Status Lights)
  Flight deck Airport Moving Maps.

## Slide 38: conclusions
Once a Sudden High Energy Runway Conflict event had been initiated, almost all of them relied upon belated visual detection from aircrew/drivers for collision avoidance.
There is currently little functionality available that will provide timely alerts involving movement on two intersecting runways.
It is concluded that there is currently a lack of an effective system of barriers that can make a significant impact in reducing the risk of collision.

## Slide 39: conclusions
Visual detection by ATC of SHERC events is limited by meteorological conditions and is unlikely to be effective once the event has been initiated.
  It is concluded that ATC training should emphasise the importance of Prevention of SHERC events; focussing on the correct use of memory aids, visual vigilance and precise ATC clearances
The use of stop bars 24H together with procedures to never cross a lit stop bar or to give a clearance across a lit stop bar could have prevented almost half of the actual serious runway incursions studied.
  It is concluded therefore that there are significant safety gains available from this established safety barrier with appropriate procedures.

## Slide 40: RECOMMENDATIONS
European ANSPs and Airport Authorities review the identified potential barriers and the conclusions of the study when they undertake operational safety analysis and improvement activities for Sudden High Energy Runway Conflict events
All European industry stakeholders support the development of procedures, tools and functionality that have the potential to prevent or mitigate the high collision risk that is present in Sudden High Energy Runway Conflicts.

## Slide 41: RECOMMENDATIONS
All European industry stakeholders promote and support the deployment and use of runway stop bars with procedures to never cross an illuminated stop bar or to give a clearance across an illuminated stop bar, subject to contingency procedures.
All European industry stakeholders to note that the consistent use of memory aids, correct and precise phraseology and visual vigilance by both ATC and Pilots/Drivers can combine to create a strong preventative barrier. Training and competence programmes should reinforce these essential activities.

## Slide 42
Thank you for your attention
Questions and Comments please