## Slide 1
“Effectiveness of implementing Industry Practice, Recommendations and Technology at Airline level”
Capt. Mattias Pak
VP Aviation Safety

## Slide 3: This presentation is not intended to present something new, but rather an example on how using risk management and recommended practices we were able to achieve good results.

## Slide 4
26 B747-400/-8
Worldwide network
Small secondary type airports
Major airports
Busiest airports of the world
0ft MSL / 9200ft MSL Airports
+500 Pilots
+30 Nationalities
+20 mother tongues
Complex Operation

## Slide 5
Taxi Procedures
Lineup Processes
Phraseology & Callouts
Training & Checking
Non-Engineered
Runway Awareness /Advisory System
EFB with NAV Charts and Own Ship Position
Moving Map with own ship position
Engineered
Runway Incursion Barriers

## Slide 6
Centered on Crew Coordination / Standard Operating Procedures
Taxi Briefing Procedures
Non-Essential tasks
Increase Situational Awareness
Taxi / Lineup
Based on ICAO
Strong SOP
Sterile Cockpit
Phraseology and Callouts
Situational Awareness
Low Visibility Taxi
Use of Engineered Barriers
Training & Checking
Non-Engineered Barriers

## Slide 7
review NOTAMS / ATIS
brief using airport diagrams (incl. hold short lines)
focus on Hot-Spots
in low visibility conditions brief CAT II/III holding points
ensure both crewmembers understand the expected taxi route
write down complex taxi clearances
an airport diagram should be readily available to each crewmember during taxi
Operations Manual
Before Taxi / Landing Procedures
Guidelines to enhance situational awareness during ground operations

## Slide 8
progressively follow taxi position
systematically verify position by signs and markings
use Moving Map
if in doubt regarding the clearance, verify taxi routing
stop the airplane if in doubt
do not allow ATC or anyone else to rush you
verify the runway is clear (both directions) and clearance is received prior entering any runway
Operations Manual
During Taxi / Landing
Guidelines to enhance situational awareness during ground operations

## Slide 9
clarify any clearances with ATC if in doubt
two flight crewmembers shall monitor and confirm clearances – this includes instructions for holding short of a runway.
read back clearly
read-back of a hold short, crossing, takeoff or landing instruction shall always include the runway designator.
Operations Manual
General
Phraseology and Callouts

## Slide 10
Low Visibility Taxi during Simulator Training
simulator Scenarios including Taxi segment
Line Checks with emphasis on phraseology
Line Checks with emphasis on SOP
Operations Manual
OM-C
Training & Checking

## Slide 11
Centered on Available Technology
The RAAS provides voice annunciations & NAV Display messages during ground operations, approach to landing, and go-around.
RAAS
Retrofitted on B747-400 with EBF Installation
EFB with NAV Charts & Own Ship Position
Factory Installed on B747-8
Moving Map with Own Ship Position
Engineered Barriers

## Slide 12
e.g. Approaching Runway (On Ground)
Approaching Runway (On Ground)
On Runway
Extended Hold On Runway
Taxiway Takeoff (advisory)
Taxiway Takeoff (caution)
Approaching Runway (Landing)
Voice Alerts
Runway Awareness and Advisory System

## Slide 13
Moving Map Display with Own Ship Position
EFB with NAV Charts & Own Ship Position
Moving Map with Own Ship Position

## Slide 14
Over simplistic Bow-Tie

## Slide 15: Conclusion
Using:
Non-Engineered & Engineered Barriers
Promoting:
High compliance of SOP
Combining:
Recommended Practices with Risk Management Procedures
SUCCESS