## Slide 1
ARSI – Advanced Runway Safety Improvement
Safety Forum 2017, Brussels, 07 June 2017

## Slide 2
Zurich Airport
10
28
34
16
14
32
RWY Crossings
RWY Intersection 16/34-10/28

## Slide 3
Safety measure I – North Flow
10
28
34
16
14
32
Performance only

## Slide 4
Safety measure II – South Flow
10
28
34
16
14
32

## Slide 5: Substantial capacity loss throughout the last years
Chart: 
| north (std) | east | south | NE winds | outbound peak
landing capacity | -0.11111 | 0 | 0 | -0.125 | 0
departure capacity | -0.12195 | 0 | -0.33333 | -0.125 | -0.16667

## Slide 6: Departure punctuality at unacceptable levels
Chart: Year
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
 | 0.817 | 0.763 | 0.809 | 0.79 | 0.79 | 0.776 | 0.764 | 0.776

## Slide 7: From best to worst in class in terms of punctuality

## Slide 8: Negative impact amplified by hub operation

## Slide 9
ARSI Principle
SWR2058 28
SWR2058 28
SWR217P 32
SWR47F 34
SWR47F 34
SWR2058 28
Line-up Clearance RWY28 SWR2058
Landing Clearance RWY34 SWR47F
Take-off Clearance SWR2058
Conflicting Clearance SWR47F / SWR2058
Take-off Clearance RWY32 SWR217P
Landing event SWR47F
Vacating RWY, Clearance completed SWR47F
Airborne SWR2058
SWR47F 34

## Slide 10
Impending Arrival Tool
Time and distance to threshold
Updated every 0.5 to 1 second

## Slide 11
Issues
Notes: ARSI functionality depends on correct controller inputs > Click as you speak > Head down time / confident that ATCOs will adopt new working method quickly
Prioritization of multiple alerts, taking into account ARSI and RIMCAS alerts > defined a clear order in which alerts are issued to ATCO
1st step: Implementation of new working methodology (February 18), 2nd step intro of alerting functions after a couple of month finetuning in shadow mode.

## Slide 12: Financial contribution linked with high expectations
Zurich Airport expects:
  Substantial increase of safety and efficiency
  Re-establish former capacity levels
  Increased and common situational awareness in daily operation
  Early implementation of PCP functionalities (airport safety nets)
Zurich Airport’s substantial contribution:
  Financial contribution of one third of overall project cost
  Update apron control systems and procedures
  Considering enhanced lightening system for pilot visualization

## Slide 13: Cooperation and innovation are key to success
Key success factors
  Close cooperation between air navigation service provider, airport operator and regulator
  Strive for options increasing both capacity and safety
  Availability of funding opportunities (national or international)

## Slide 14: Questions & Answers